## Slide 1: EEG Preprocessing Tutorial
CCPL - Lyndon Rakusen

## Slide 2: Our Datasets/Projects
Mammography EEG
  Radiologists
  Naives Training
Attentional Blink EEG
  Dots
  Scenes

## Slide 3: Mammography EEG Design
400 trials total (+30 practice)
Four different kinds of mammogram stimulus:
  160 Normal (no cancer)
  60 Obvious
  60 Subtle
  120 Global (Prior/Contralateral)
Each trial consists of a unilateral mammogram for 500 ms, a mask for 500 ms, a response window of 2 seconds, and a jittered ISI between 1 and 2 seconds.
Participant responded Abnormal or Normal (yes or no)

## Slide 4: Mammography EEG Design
Radiologists
  5 experienced mammographers from York hospital
  1 EEG test session
Naives
  15 participants
  2 EEG test sessions, 9 online training sessions
Baseline start: -0.4s, Baseline end: -0.2s
Event start: 0s, Event end: 2.0s

## Slide 5: Attentional Blink EEG Experiments
36 participants (mainly students)
Four conditions with multiple levels:
  Scenes or dots
  Selective (S) or non-selective (NS)
    S-NS, NS-S, S-S, and NS-NS
  Identify scene vs object
  Time lag 1, 2, 3, and 4

## Slide 8: Attentional Blink Dots
Predominant colour (NS)
  Red, green, blue, or pink
Bisected dot (S)
  Green half: left or right

## Slide 9: EEG Data: The Basics
64 electrodes/channels
  Measuring tiny charges on the scalp
1 reference channel (Cz)
  Subtracted from the other channels
1 eye channel (EOG)
  Measures blinks for cleaning signal later
Time locked triggers/events sent from the testing PC

## Slide 10: Preprocessing Ingredients
Raw EEG data files (.fif)
Trigger files (.trg)
Montage file (.xyz)
Behavioural data (.csv)

## Slide 11: Other Ingredients
EEGTraining_Sessions.py
Participant list .csv file with the header:
  ppt_num, data_path, extra_events_path, pid, EOG_channel, status, ref_channel, raw_format
trigger labels .csv file with the header:
  label, value, active
EEGpykit project - a module created by me
  https://github.com/llr510/EEGpykit
A preprocessing output directory
  e.g 'output_directory/'

## Slide 12: Preprocessing - The Hard Way
MATLAB
  Brainstorm
    GUI based preprocessing (and analysis)
    https://neuroimage.usc.edu/brainstorm/Installation
    https://neuroimage.usc.edu/brainstorm/Tutorials

## Slide 13: Preprocessing Tools
Python >=3.8:
  Miniconda - https://docs.conda.io/projects/miniconda/en/latest/
  Pycharm Community Edition - https://www.jetbrains.com/pycharm/download/
  MNE - https://github.com/mne-tools/mne-python

## Slide 14: A Brief Python Aside
Python is a programming language and has:
  Variables - store information under a name
    my_var_can = integers, strings, lists, arrays, other variables, pretty much anything
  Maths - it’s a big fancy calculator
    +, -, *, /, **, math.sqrt()
  Logic - do a thing if the right conditions are met
    if, elif, else
  Loops - do a thing multiple times
    for, while
  Functions - reuse the same bit of code in different places without writing it all out again
    def(some, arguments), return
  Modules - reuse you own and other people’s scripts
    import
    “Yo dawg, I heard you like code so we loaded code into your code so you can run code while you code”
https://www.w3schools.com/python/

## Slide 15: EEGpykit Module Requirements
Module | Suggested Version | Notes
mne | 1.1.1 | 
mne-faster | 1.1 | 
numpy | 1.23.3 | issues when using in conda environment
scikit-learn | 1.1.2 | 
pandas | 1.5.0 | 

## Slide 16: Creating a Python Environment

## Slide 17: Pre-preprocessing
EEGTraining_Sessions.py
  Used to create labelled event file from behavioural data + trigger files
    Columns: label, event time
Will be used to label Epochs
+
=

## Slide 18: MNE Terminology
Objects:
  Raw - continuous EEG recording.
  Epoch - raw data split into pieces time locked to event.
  Evoked - average of multiple epochs.

## Slide 19: Automatic EEG Preprocessing with FASTER and MNE
Lyndon Rakusen

## Slide 20: Read, resample, and bandpass raw
Bandpass (iir): 0.5 Hz – 40 Hz
Sample rate: 1000 Hz to 200 Hz
  (upper limit of activity is ~100 Hz)
Add montage

## Slide 21: Read, resample, and bandpass raw
Bandpass (iir): 0.5 Hz – 40 Hz
Sample rate: 1000 Hz to 200 Hz
  (upper limit of activity is ~100 Hz)
Add montage

## Slide 22: Frequencies & Sampling

## Slide 23: Split into Epochs with custom events
For Attentional Blink EEG:
  Baseline (-200ms)
  Event & Baseline end (0ms)
  Epoch end (+800ms)
Set EEG reference (average)

## Slide 24: Power Spectral Density (PSD) of Epochs Before

## Slide 25: Evoked Before

## Slide 26: The FASTER Protocol
Step 1: mark bad channels
  Variance, correlation, hurst, kurtosis, line noise
  Interpolate
Step 2: mark bad epochs
  Amplitude, deviation, variance
  Drop
Step 3: mark bad ICA components
  EOG
  Subtract
Step 4: mark bad channels for each epoch
  Amplitude, deviation, variance, median gradient, line noise
  Interpolate
Extra step 40Hz FIR filter
https://www.sciencedirect.com/science/article/pii/S0165027010003894

## Slide 27: Power Spectral Density (PSD) of Epochs Before

## Slide 28: Power Spectral Density (PSD) of Epochs After

## Slide 29: Evoked Before

## Slide 30: Evoked After

## Slide 31: Running EEGpykit.preprocessor
Has a handy run GUI.
leave additional_events_fname blank.
Will bandpass filter all data first, then it will FASTER preprocess data.

## Slide 32: Preprocessing Output
3 files per participant/session:
  Report file (.html)
    Has figures and stats from preprocessing
  Preprocessed epochs - (.epo.fif)
    Can be opened in Brainstorm with some event label finagling…
    Used for our MVPA analysis
  Preprocessed pickle file (.pickle)
    Most likely won’t need this, but also contains filtered raw and epochs.
    Can be read in python

## Slide 33: EEG Analysis Tutorial
CCPL - Lyndon Rakusen

## Slide 34: Analysis with MVPA
Multivariate Pattern Analysis (or Multi Voxel in fMRI)
Behaviour and stimuli have neural representations.
  Therefore theoretically we can discriminate between neural activity in one condition vs another.
Broad term for lots of similar techniques.
We’ll be using my script: EEGpykit/MVPA/MVPA_analysis.py
  https://mne.tools/stable/auto_tutorials/machine-learning/50_decoding.html#temporal-decoding

## Slide 35: SVM
Support vector machines (SVMs)
  Draws an hyperplane that optimally divides the data into groups.
    e.g. a 1d line in 2d space, a 2d line in 3d space, etc.
Our EEG data is:
  Epochs x Channels x Times

## Slide 36: Sliding Estimator
X: Fit an SVM to epochs x channel data, for each time point.
y: Each epoch is assigned a value of 1 or 0, depending on what condition it belongs to.
The SVM tries to determine which condition the epoch belongs to for each time point.
Derive AUC (area under ROC curve) score for each time point.

## Slide 37: Sliding Estimator
If the SVM can discriminate between conditions we should see higher than chance (0.5) after times 0.
We could do this for each participant and plot the average curve and error.

## Slide 38: Group MVPA Analysis
Two options:
  Fit a sliding estimator to each participant - average the result
  OR
  Fit a sliding estimator to all the data

## Slide 39: LOGO Cross Validation
Leave One Group Out
The Sliding Estimator is trained on every participant except one
The estimator model is tested on the data from the participant that is ‘left out’
Everyone gets a turn at being the test data
The results are the average test scores across time
Test
Train

## Slide 40: Group MVPA Analysis
Which should look something like this:
Can’t detect a difference
Can detect a difference
Can detect a difference but not as consistently

## Slide 41: An Example Analysis
Does viewing a normal mammogram elicit a different response to an abnormal mammogram?
  Condition 1: [‘Normal’]
  Condition 2: [‘Obvious’, ‘Subtle’]

## Slide 42: Signal Analysis
What does the data look like?
Calculate the absolute difference between conditions
Plot a new line that is the difference
When done for every channel you get a grid
Chart: 
| -0.4 | 0 | 0.5 | 1.0
Conditon 1 | 0.1 | 0.75 | 0 | 0.5
Conditon 2 | -0.1 | -0.5 | 0.3 | 0.4
+ΔµV
Condition 1
Condition 2
-ΔµV